## Slide 1
Water Supply Systems: Water Budgets and Groundwater Assessments

## Slide 2
Three Quantitative Pieces
1. Hydrologic Budgets
2. Darcy’s Law
3. Theis Equations

## Slide 3: The Water Budget
INFLOW = OUTFLOW +/- CHANGE IN STORAGE
Inflows: Precipitation + SW inflow + GW inflow + imported water
Outflows: ET + SW out + GW out + Exports + consumption
Storage: Increased/decrease in SW storage + increase/decreases in GW storage
Notes: http://www.unep.org/dewa/vitalwater/index.html
Evapotranspiration (ET) is the sum of evaporation and plant transpiration from the Earth's land and ocean surface to the atmosphere.

## Slide 4: Darcy’s Law
Darcy: Made first systematic study of movement of water through a porous medium and the first to state the simple law describing GW flow (1856)
Q = K
Head Difference
Distance between Heads
Area = KiA
Q = Volumetric discharge (L3/t)
i = Hydraulic Gradient (L/L)
K = Hydraulic conductivity (L/t)
Notes: Hydraulic head : a measure of the potential of water at the measurement point
Hydraulic head is a measurement of the total mechanical energy per weight of the groundwater flow system. In other words, it is the fluid potential for flow through porous media. It is predominantly comprised of pressure and elevation heads.
Hydraulic conductivity: a soil’s ability to transmit water when subjected to a gradient

## Slide 5: Theis Equations
Theis: set of equations that describe the amount of drawdown created by a pumping well over a specific time period
S = drawdown at any time and distance from a pumping well (L)
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
W(u) = Theis well function (unitless)
S =
Q
4πT
W(u)
Notes: Transmissivity: rate of flow of water through a vertical strip of an aquifer

## Slide 6: The Water Budget
The relationship between inputs and outputs of water through a region
Uses principles of conservation of mass in a closed system
Can help to manage a water supply
Notes: This equation uses the principles of conservation of mass in a closed system, whereby any water entering a system (via precipitation), must be transferred into either evaporation, surface runoff (eventually reaching the channel and leaving in the form of river discharge), or stored in the ground. This equation requires the system to be closed, and where it isn't (for example when surface runoff contributes to a different basin), this must be taken into account.

## Slide 7: The Water Budget
Can be calculated for any domain:
  Atmosphere
  Ocean
  Continent
  Watershed: MOST TYPICAL
  Stream segment
  Lake
  Geopolitical entities (state, country, etc.)
Notes: http://www.unep.org/dewa/vitalwater/index.html

## Slide 8: Water Budget for Watershed
Watershed: A watershed is an area of land that drains all the streams and rainfall to a common outlet such as the outflow of a reservoir, mouth of a bay, or any point along a stream channel.
Notes: USGS: A watershed is an area of land that drains all the streams and rainfall to a common outlet such as the outflow of a reservoir, mouth of a bay, or any point along a stream channel. The word watershed is sometimes used interchangeably with drainage basin or catchment.

## Slide 9: The Water Budget
TERMS
Precipitation: Any form of solid or liquid water that falls from the atmosphere to the Earth’s surface
Evapotranspiration: Process that returns water back to the atmosphere
  Evaporation from open water (lakes, etc.)
  Evaporation from soils (deserts, mountains, etc.)
  Transpiration from plants (evaporation from within leaves)
Groundwater: water held underground in the soil or in pores and crevices in rock
Surface Water: water that has not penetrated below the surface of the ground
Notes: http://www.unep.org/dewa/vitalwater/index.html
Evapotranspiration (ET) is the sum of evaporation and plant transpiration from the Earth's land and ocean surface to the atmosphere.

## Slide 10: Setting up a Water Budget Equation
Similar to accounting for your personal finances
  Track income and expenses
  See change in “storage” of your bank account
All inputs, outputs, and changes must be identified
What is your conceptual model??
What are the uncertainties?
Notes: Conceptual model: a type of diagram which shows of a set of relationships between factors that are believed to impact or lead to a target condition; a diagram that defines theoretical entities, objects, or conditions of a system and the relationships between them

## Slide 11: The Water Budget
INFLOW = OUTFLOW +/- CHANGE IN STORAGE
Inflows: Precipitation + SW inflow + GW inflow + imported water
Outflows: ET + SW out + GW out + Exports + consumption
Storage: Increased/decrease in SW storage + increase/decreases in GW storage
Notes: http://www.unep.org/dewa/vitalwater/index.html
Evapotranspiration (ET) is the sum of evaporation and plant transpiration from the Earth's land and ocean surface to the atmosphere.

## Slide 12: Water Budget for Upper Feather River Watershed
Area: 3,600 mi2 ≈ 9,300 km2
Average precipitation = 45 inches/year
Average ET = 20 inches/year
SW inflows:
SW Outflows: 2.3% of total inflows ≈ 122.13 cfs
Notes: Located in northern California
Feather River: main water supply to the Oroville Reservoir
  State Water Project
  Provides water to over 25 million Californians
  Can store 3.5 MAF

## Slide 13: Water Budget for Upper Feather River Watershed
Average exports from Oroville Reservoir: 2.8 MAF
Average change in GW storage: 3 inches/year
Assumptions:
  No GW inflow or outflow
  No imported water
  Exports of Oroville Reservoir = total watershed exports
What is the change in surface water storage in MAF per year???

## Slide 14: The Water Budget
INFLOW = OUTFLOW +/- CHANGE IN STORAGE
Inflows: Precipitation + SW inflow + GW inflow + imported water
Outflows: ET + SW out + GW out + Exports + consumption
Storage: Increase/decrease in SW storage + increase/decrease in GW storage
Notes: http://www.unep.org/dewa/vitalwater/index.html
Evapotranspiration (ET) is the sum of evaporation and plant transpiration from the Earth's land and ocean surface to the atmosphere.

## Slide 15: The Water Budget
Helpful Conversions:
1 foot = 12 inches
1 mile = 5,280 ft
  1 mile2 = 2.7x107 ft2
1 Acre = 43,560 ft2
Notes: http://www.unep.org/dewa/vitalwater/index.html
Evapotranspiration (ET) is the sum of evaporation and plant transpiration from the Earth's land and ocean surface to the atmosphere.

## Slide 16
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
OUTFLOWS:
ET + SW out + GW out + Exports
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 17
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
XXXX AFY +
OUTFLOWS:
ET + SW out + GW out + Exports
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 18
Precipitation:
45 inches/year…..how to get this in AFY?
Note: Area = 3,600 mi2

## Slide 19
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + XXXX AFY
OUTFLOWS:
ET + SW out + GW out + Exports
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 20
SW Inflows:
5,301 cfs
*Note: The snowmelt contribution to the streamflow is included in this estimate

## Slide 21
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + XXXX AFY + XXXX AFY
OUTFLOWS:
ET + SW out + GW out + Exports
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 22
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 23
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
XXXX AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 24
Evapotranspiration:
20 inches/year
Note: Area = 3,600 mi2

## Slide 25
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + XXXX AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 26
SW Outflows:
122.31 cfs

## Slide 27
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + 8.85x104 AFY + XXXX AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage
Δ SW Storage + 109.09 AFY

## Slide 28
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + 8.85x104 AFY + 0 AFY +XXXX AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage

## Slide 29
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + 8.85x104 AFY + 0 AFY + 2.8x106AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage
XXXX AFY

## Slide 30
Change in GW Storage:
3 inches/year
Note: Area = 3,600 mi2

## Slide 31
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + 8.85x104 AFY + 0 AFY + 2.8x106AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage
Δ SW Storage + 5.74x106 AFY

## Slide 32
INFLOWS:
Precipitation + SW inflow + GW inflow + Imported water
8.62x106 AFY + 3.83x106 AFY + 0 AFY + 0 AFY = 12453451.25 = 1.25x107 AFY
OUTFLOWS:
ET + SW out + GW out + Exports
3.83x106 AFY + 8.85x104 AFY + 0 AFY + 2.8x106AFY = 6722340.86 = 6.72x106 AFY
STORAGE:
Change (Δ) in SW Storage + Change (Δ) in GW Storage
Δ SW Storage + 5.74x106 AFY

## Slide 33
INFLOW = OUTFLOW +/- CHANGE IN STORAGE
12453451.25 AFY = 6722340.86 AFY + 5379669.42 AFY + ΔSW Storage
12453451.25 AFY = 12102010.28 AFY +ΔSW Storage
ΔSW Storage = 351440.97 AFY or 0.35 MAFY
ΔSW Storage = 0.35 MAF per year

## Slide 34: Analysis
So what does this change in storage mean?
What would happen in a drought year or during multiple drought years?
How can this information be used for supply management?
  What else would reservoir operators need to know?

## Slide 35: Groundwater Sustainability
Definition: groundwater use that can be maintained for an indefinite time without causing enviornmental, social, or economic adverse consequences
  Jason Gurdak (my Hydrogeology professor at SFSU)

## Slide 36: Groundwater Resources
Aquifer: a layer of rock, sand, or earth that contains water or allows water to pass through it.

## Slide 37: Groundwater Resources

## Slide 38: California’s Groundwater
Notes: Need to look up geological history of the region

## Slide 39: California’s Groundwater

## Slide 40: California’s Groundwater
Groundwater contributes to approximately 38% of CA water supply
  46% in drought years
  75% estimated for 2014
    5.1 MAF of the 6.6 average availability
Notes: Groundwater resources play a vital role in maintaining California's economic and environmental sustainability. During an average year, California's 515 alluvial groundwater basins and subbasins contribute approximately 38 percent toward the State's total water supply. During dry years, groundwater contributes up to 46 percent (or more) of the statewide annual supply, and serves as a critical buffer against the impacts of drought and climate change. Many municipal, agricultural, and disadvantaged communities rely on groundwater for up to 100 percent of their water supply needs. Groundwater extraction in excess of natural and managed recharge has caused historically-low groundwater elevations in many regions of California.

## Slide 41: Groundwater Pumping
Subsidence: Land subsidence is the lowering of the land-surface elevation from changes that take place underground
  Common causes:
    Pumping of water, oil, gas
    Dissolution of limestone aquifers
    Collapse of underground mines
Left: Location of 1977 maximum subsidence in the United States identified by Dr. Joseph F. Poland (pictured). Signs on pole show approximate altitude of land surface in 1925, 1955, and 1977. San Joaquin Valley southwest of Mendota, California. Credit: Dick Ireland, USGS.

## Slide 42: Data Needs for Sustainable Groundwater Mgmt
  Soil type
  Water table level
  Number of wells
  Pumping rates
  What else????
How do we simplify a complex system?

## Slide 43: Sustainable Groundwater Management Act
  Comprehensive bill passed in 2014 that is the first in the state to regulate groundwater
  Requires formation of local GW sustainability agencies (GSAs) that create and help to adopt long-term GW sustainability plans:
  GSA must:
    Register GW wells
    Measure and manage extraction
    Generate reports
  Designates medium and high priority basins

## Slide 44
Water Supply Systems: Water Budgets and Groundwater Assessments
Notes: Hello my name is Amber McCullum and I am a PhD Candidate at the University of California, Santa Cruz in the Environmental Studies Department. I am primarily advised by my co-authors, Dr. Brent Haddad and Dr. Renée Kidson.
Today I will be discussing the “Application of Empirical Mode Decomposition or EMD for Identification and Characterization of Long-run persistence in California reservoir inflows”.

## Slide 45: Groundwater Management
Two really important concepts:
  Darcy’s Law: Movement of water through a porous medium
  Theis equation: drawdown of water created by a pumping well
1856: Darcy’s Law
1929: Theis equations
Notes: Darcy: French engineer: As a member of the Corps, he built an impressive pressurized water distribution system in Dijon following the failure of attempts to supply adequate fresh water by drilling wells. Chief engineer for water department
Charles V. Theis graduated with a PhD from the University of Cincinnati in June 1929 and made numerous contributions to the field of ground water science throughout his life.

## Slide 46: Darcy’s Law
Darcy: Made first systematic study of movement of water through a porous medium and the first to state the simple law describing GW flow (1856)
Q = K
Head Difference
Distance between Heads
Area = KiA
Q = Volumetric discharge (L3/t)
i = Hydraulic Gradient (L/L)
K = Hydraulic conductivity (L/t)
Notes: Hydraulic conductivity: a soil’s ability to transmit water when subjected to a gradient
Hydraulic head : a measure of the potential of water at the measurement point

## Slide 47: Theis Equation
Theis: set of equations that describe the amount of drawdown created by a pumping well over a specific time period
S = drawdown at any time and distance from a pumping well (L)
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
W(u) = Theis well function (unitless)
S =
Q
4πT
W(u)

## Slide 48: Groundwater Terminology
Infiltration: Water entering the soil across the land/atmosphere interface
Recharge: Flux of water to the water table
Water Table: Depth at which the soil becomes fully saturated

## Slide 49: Groundwater Terminology
Unconfined Aquifer: are those into which water seeps from the ground surface directly above the aquifer
Confined Aquifer: are those in which an impermeable dirt/rock layer exists that prevents water from seeping into the aquifer from the ground surface located directly above.

## Slide 50: Groundwater Terminology
Potentiometric surface: The level to which water rises in a well
  In a confined aquifer this surface is above the top of the aquifer
  In unconfined aquifer it is the same as the water table
Notes: The potentiometric surface is the level to which water rises in a well. In a confined aquifer this surface is above the top of the aquifer unit; whereas, in an unconfined aquifer, it is the same as the water table.
As you might expect, a potentiometric map is a contour map of the potentiometric surface. As on the surface of the earth, water flows from high elevation, or potential, to low elevation. Thus a potentiometric map indicates which direction water is moving in the subsurface.

## Slide 51: Groundwater Terminology
Porosity: fraction of soil occupied by void spaces
  These spaces can be filled with water: determines maximum water holding capacity of a soil
Permeability: how easily water can flow through porous soil or bedrock

## Slide 52: Groundwater Terminology
Soil Water Content: Amount of water contained in a soil
  When soil is “saturated” the volumetric water content = porosity
  Can be expressed as:
    Volumetric water content
    Gravimetric water content
    Saturation ratio
  Most often volumetric
  Volume of water
  Volume of soil

## Slide 53: Groundwater Terminology
Hydraulic head : the potential of water at the measurement point
  Water flows from high to low hydraulic head
  Generally expressed as a gradient in units of length

## Slide 54: Groundwater Terminology
Hydraulic gradient: Change in total head divided by the distance over which the change occurs
  it causes water to move

## Slide 55: Groundwater Terminology
Hydraulic conductivity: a soil’s ability to transmit water when subjected to a gradient
  Expressed as length/time
  Related to permeability

## Slide 56: Groundwater Terminology
Transmissivity: rate of flow of water through a vertical strip of an aquifer
  Expressed as area per unit time
Transmissivity = Hydraulic Conductivity x Aquifer Thickness
Notes: Transmissivity: rate of flow of water through a vertical strip of an aquifer

## Slide 57: Groundwater Terminology
Drawdown: change in hydraulic head caused by well pumping
Cone of Depression: cone-shaped lowering of water observed in an aquifer caused by drawdown

## Slide 58: Darcy’s Law
Darcy: Made first systematic study of movement of water through a porous medium and the first to state the simple law describing GW flow (1856)
Q = K
Head Difference
Distance between Heads
Area = KiA
Q = Volumetric discharge (L3/t)
i = Hydraulic Gradient (L/L)
K = Hydraulic conductivity (L/t)

## Slide 59: Darcy’s Law
Q = K
Head Difference
Distance between Heads
Area = KiA

## Slide 60: Darcy’s Law
Q = K
Head Difference
Distance between Heads
Area = KiA
K = 0.01 cm/s

## Slide 61
What is the discharge in this aquifer in cubic feet per year?
…Or what is the volume of water flowing through the aquifer area per year??
Conversion Reminder:
1 m = 100 cm
1 m3 = 35.3 ft3

## Slide 62: Darcy’s Law
Q = K
Head Difference
Distance between Heads
Area = KiA
K = 0.01 cm/s
Conversion Reminder:
1 m = 100 cm
1 m3 = 35.3 ft3

## Slide 63: Darcy’s Law
Q = K
Head Difference
Distance between Heads
Area = KiA
Q = 0.01 cm/s
(0.4 m – 0.21 m)
0.63 m
(6 cm x 0.75 cm)
K = 0.01 cm/s
Q = 0.01 cm/s
(0.19 m)
0.63 m
(4.5 cm2)
Q = 0.013 cm3/s or 1.3 x10-8 m3/s

## Slide 64: Darcy’s Law
1 m3 = 35.3 ft3
Convert discharge to cubic feet per year
Q = 1.3x10-8 m3/s

## Slide 65: Theis and HW Review
Notes: Conceptualization of radial flow to a fully penetrating pumping well: shows initial and pumping pot1ntiometric surfaces. Two observation wells at r1 and r2: show differences in spatial drawdowns in s1 and s2. Aquifer tickness is b

## Slide 66: Theis Equation Parameter
r = radial distance from the pumping well to any distance (L)
S = coefficient of storage (L3/L3)
T = transmissivity of the aquifer (L2/t)
t = elapsed time since pumping began (t)
u = Theis equation parameter (unitless)

## Slide 67: Theis Equation
Theis: set of equations that describe the amount of drawdown created by a pumping well over a specific time period
s = drawdown at any time and distance from a pumping well (L)
ho = initial hydraulic head before pumping
h = hydraulic head at the same distance after some elapsed time
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
u = Theis equation parameter

## Slide 68: Theis Equation
s = drawdown at any time and distance from a pumping well (L)
ho = initial hydraulic head before pumping
h = hydraulic head at the same distance after some elapsed time
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
u = Theis equation parameter
W(u) = Theis well function (unitless)
We can solve for integral using this expansion = W(u)

## Slide 69: Theis Equation
What does this mean????
2*(1*2) +
3*(1*2*3) -
4*(1*2*3*4)
Notes: Factorials!

## Slide 70: Theis Equation
s = drawdown at any time and distance from a pumping well (L)
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
u = Theis equation parameter (unitless)
W(u) = Theis well function (unitless)

## Slide 72
Q =
T =
S =
r =
t =
Discharge =
Transmissivity =
Storage Coefficient =
900 gpm Convert to ft3/day
35,200 gpd/ft Convert to ft2/day
0.00072
7,500 ft
40 years Convert to days
distance from pumping well =
time =
Helpful Conversion
1 gallon = 0.134 ft3
Notes: Open up the HW pdf and show them the equations we just talked through.
Then, open up the 3.1 excel sheet:
Look at introduction
Have them name the parameters based on the paragraph: write those on the board
Talk through conversions of those parameter

## Slide 73
In groups: Create excel calculation for the Theis parameter (u), the Theis well function (W(u), and the drawdown (s)
r = radial distance from the pumping well to any distance (L)
S = coefficient of storage (L3/L3)
T = transmissivity of the aquifer (L2/t)
t = elapsed time since pumping began (t)
u = Theis equation parameter (unitless)
W(u)
2*(1*2) +
3*(1*2*3) -
4*(1*2*3*4)

## Slide 74
Conversions:
Q = 900 gpm (gallons per minute) into ft3/day
1 gallon = 0.134 ft3

## Slide 75
Conversions:
T = 35,200 gpd/ft (gallons per day per foot)
1 gallon = 0.134 ft3

## Slide 76
Conversions:
t = 40 years

## Slide 77
In groups: Create excel calculation for the Theis parameter (u)
r = radial distance from the pumping well to any distance (L)
S = coefficient of storage (L3/L3)
T = transmissivity of the aquifer (L2/t)
t = elapsed time since pumping began (t)
u = Theis equation parameter (unitless)
How did you create this calculation in excel?

## Slide 78
Now, calculate entire W(u) term:
How did you create this calculation in excel?

## Slide 79
Next, calculate S for the 40 year period in excel
s = drawdown at any time and distance from a pumping well (L)
Q = discharge from pumping well (L3/t)
T = transmissivity of the aquifer (L2/t)
u = Theis equation parameter (unitless)
W(u) = Theis well function (unitless)
How did you create this calculation in excel?

## Slide 80
For the next steps in the homework you will need to change the distance from the pumping well to see what the cone of depression looks like.
If you have your excel equations programmed correctly and you change the r value, the other parameters (u, W(u), and s) will change.
Then, fill in the W(u) values into that portion of the spreadsheet and fill in each value of s into Table 1 and 2 as the distances change.
This will automatically create the drowndown figures below